## Slide 1
Lata Pasupulety
Department of Science and Humanities
ENGINEERING CHEMISTRY

## Slide 2
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Class content:
Concentration cells
  Types of concentration cells
    Electrolyte concentration cells
    Electrode concentration cells
Ion- selective electrodes
  Types of ion – selective electrodes
  Electrode potential for an ion-selective electrode

## Slide 3
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Concentration cells:
An electrochemical cell in which identical electrodes are in contact with a solution of identical species but of different concentration
https://chemdemos.uoregon.edu/demos/Voltaic-Cell-CuCu-concentration-cell-Demonstration

## Slide 4
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
In this cell 2 copper electrodes are immersed in copper sulphate
solutions of concentration c1 & c2 , such that c2> c1
An electrolyte has spontaneous tendency to diffuse from a
solution of higher concentration to a solution of lower
concentration which is the driving force for development of
potential
Oxidation takes place at anode and reduction takes place
at cathode
e.g.,Cu/Cu2+(c1)//Cu2+(c2)/Cu

## Slide 5
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Reactions :
At anode: Cu  Cu2+ (c1)+2e-
At cathode: Cu2+ (c2)+ 2e- Cu
Expression for cell potential:
The emf of the cell = E cathode – E anode

## Slide 6
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
The emf of the cell is positive only if c2 > c1
i.e., conc of metal ion at cathode > conc. of metal ion at anode
The emf of the cell depends upon the ratio c2/c1
When c2 = c1, the emf of the cell becomes zero
During working of the cell, concentration of ions
increases at anode decreases at cathode
When current is drawn from the cell c1 increases and
c2 decreases
The cell can operate only as long as the
concentration terms are different

## Slide 7
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Types of concentration cells:
Electrolyte concentration cell
Electrode concentration cell
Electrolyte concentration cell:
Electrolyte concentration cell consists of two same electrodes that are dipped in the same electrolyte but with different concentrations of electrolytes
Cu/Cu2+(c1)//Cu2+(c2)/Cu
Cell potential is given by
Electrode concentration cell
Electrode concentration cell consists of two identical electrodes of different activity which are dipped in the same solution of electrolyte
Na-Hg(c1)/Na+/Na-Hg(c2)
Cell potential is given by

## Slide 8
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Na-Hg(c1)/Na+/Na-Hg(c2) :
Reactions are :
At anode: Na-Hg(c1)  Na+ + e-
At cathode: Na+ + e- Na-Hg(c2)
Cell potential = E cathode – E anode

## Slide 9
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Pt/H2(p1 atm)/H+/H2(p2 atm)/Pt :
Nernst Equation:
Pt/Cl2(p1 atm)/Cl-/Cl2(p2 atm)/Pt :
Nernst Equation:

## Slide 10
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Ion selective electrodes (ISE)
Selectively respond to a specific ion in a mixture
Potential developed is a function of concentration of that ion
Have a membrane which is capable of exchanging the specific ion with solution with which it is in contact
Membrane electrodes
e.g., glass electrode

## Slide 11
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Types of Ion selective electrodes :
Electrodes are classified based on the membrane material
Crystalline / solid state membrane electrodes:
Single crystal LaF3 selective to F-
Polycrystalline such as Ag2S selective to S2-
Non-crystalline membrane electrodes:
e.g., Glass membrane selective to H+ , Na+
Liquid membrane electrodes:
An ion-exchanger is dissolved in a viscous organic liquid
membrane; used for Ca+, K+
Immobilised liquid in a rigid polymer:
e.g., immobilized ion exchanger in PVC matrix ; used for Ca+, NO3-

## Slide 12
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Electrode potential of an ion-selective electrode
Schematic representation:
analyte solution reference solution inner reference electrode
[Mn+] = C1 [Mn+] = C2
boundary potential is
since concentration of reference solution C2 is constant
where

## Slide 13
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
Overall potential of the membrane electrode is given by
EM = Ej + Eref
since
where EoM = K + Eref
At 298K,
Membrane electrode is coupled with an external reference electrode

## Slide 14
ENGINEERING CHEMISTRY
Module 4- Electrochemical equilibria
External ref. electrode/Analyte/membrane/ ref. solution/Internal ref. electrode
Cell potential = E cathode – E anode
E cell = E membrane – E ext.ref.electrode
E cell can be measured, E ext.ref.electrode is known
E membrane can be determined
Since , C1 can be determined
The disadvantage of an ion-selective electrode is that the membrane offers very high resistance so ordinary potentiometers cannot be used; special type of potentiometers have to be used.
Applications :
Used to determine concentration of number of cations and anions such as H+, Li+,Na+,K+,Pb2+,Cu2+,Mg2+,CN-, NO3-, F-etc

## Slide 15
Lata Pasupulety
Department of Science and Humanities
latapasupulety@pes.edu
+91 80 6666 3333 Extn 759
THANK YOU