## Slide 1
Asha A
Department of Science and Humanities
ENGINEERING CHEMISTRY

## Slide 2
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Class content:
Corrosion control
  Cathodic protection
    Sacrificial anode method
    Impressed cathodic current method

## Slide 3
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Cathodic protection:
By converting it completely into cathode and no part of it is allowed to act as anode
Cathode does not undergo corrosion so the structure is protected
Cathodic protection
Sacrificial anode method
Impressed current method

## Slide 4
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Sacrificial anode method:
  In this method, protected metal structure is converted into a
  cathode by connecting it to a more active metal
  This active metal (example: zinc, magnesium) acts as
  an auxiliary anode
  These metals being more active, acts as anode and undergo
  preferential corrosion, protecting the metal structure
  Since the anodic metals are sacrificed to protect the metal
  structure, the method is known as sacrificial anode method
  Exhausted anodes have to be replaced periodically

## Slide 5
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Examples:
Mg/Zn bars are fixed to the sides of ocean going ships to act as sacrificial anodes
Mg/Zn blocks are connected to buried pipe lines
A Mg block connected to a buried oil storage tank
Source:https://www.pipelineprotection.co.uk/services/cathodic-protection/
Source:https://thenavalarch.com/ship-corrosion-cathodic-protection-sacrificial-anodes/

## Slide 6
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Advantages:
The method is simple
Low installation cost
Does not require power supply
Disadvantages:
Involves recurring expenditure for replacement of consumed
anodes

## Slide 7
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Impressed current method:
By applying a direct current
The protected metal is made cathodic by connecting it to the cathode
of the external source of current
Anode of the external source is usually connected to an inert electrode
like graphite; Platinum, silicon, iron are also used as anodes
A backfill of coke ,bentonite is used to improve efficiency of the anode
The metal structure being cathode does not undergo corrosion
Anode being inert remains unaffected

## Slide 8
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Source:https://www.mcwaneductile.com/blog/v-bio-r-or-cathodic-protection-an-honest-comparison/
Source:https://www.sciencedirect.com/topics/engineering/impressed-current-system

## Slide 9
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Advantages:
One installation can protect large area of metal
Limitations:
Rather expensive, since it needs high current for safe protection of structure
If the impressed current is not uniform on the entire surface of the protected structure, localized corrosion takes place on the protected metal

## Slide 10
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
If hydrogen liberation is the cathodic reaction on the metal surface, then the protected metal may suffer from hydrogen embrittlement
Hydrogen embrittlement:
H2 molecule being small enters the metal lattice and when the pressure increases , it causes blisters and makes the metal brittle

## Slide 11
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Class content:
Corrosion control
  Anodic Protection
    Impressed current method

## Slide 12
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Anodic protection:
Prevention of corrosion by impressed anodic current is called as anodic protection
The article to be protected is made anode by connecting it to the anode terminal of the power source
Can be used only for metals which show active-passive behaviour like nickel, iron, chromium, titanium and their alloys
On applying an optimum potential these metals get passivated and rate of corrosion decreases

## Slide 13
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Active – passive transition of metals with the application of a potential can be explained from the potential-current curve
Passive region
Transpassive region
E
Ep
log i
icrit
ipassive

## Slide 14
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
A known potential is applied to the metal specimen and current is measured
As the potential is increased, initially the current also increases, and it indicates the dissolution of metal
This trend continues until the current reaches a critical value (icrit) and passivation due to the development of oxide layer sets in
The potential required for the passivation due to the development of oxide layer, this potential called passivating potential (Ep)
Passive region
Transpassive region
E
Ep
log i
icrit
ipassive

## Slide 15
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Above Ep, the current flow decreases and reaches a minimum value called passivation current, ipassive
If the potential is increased further, the metal remains unattacked up to a particular potential is reached. In this range, corrosion rate of the metal is very small. This potential range, in which anodic potential can be achieved, is called passive region
If the potential is increased further, corrosion rate increases and this region is called the transpassive region
The optimum potential for protection is determined by electrochemical measurements
Passive region
Transpassive region
E
Ep
log i
icrit
ipassive

## Slide 16
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Anodic protection to a structure is applied by using a device
called potentiostat
It is an electronic device that maintains a metal at a constant potential with respect to a reference electrode
Potentiostat has three terminals, one connected to the anode, another to an auxillary cathode(Pt) and the third connected to a reference electrode

## Slide 17
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Anodic protection of a steel tank carrying H2SO4
Source:https://uomustansiriyah.edu.iq/media/lectures/5/5_2016_04_20!11_15_38_AM.pdf
One terminal is connected to the storage tank(anode)
Other is connected to the reference electrode and a constant potential corresponding to the passive range is maintained between tank and the reference electrode
The third terminal is connected to an auxiliary electrode like Pt

## Slide 18
ENGINEERING CHEMISTRY
Module 6- Corrosion Chemistry
Advantages:
Applicability in extremely corrosive environments
Low current demand
Disadvantages:
Restricted to metals that show active-passive behaviour
Initial installation cost is high
Cannot reduce corrosion rate to zero unlike cathodic protection

## Slide 19
Asha A
Department of Science and Humanities
THANK YOU