## Slide 1
Asha A
Department of Science and Humanities
ENGINEERING CHEMISTRY

## Slide 2
ENGINEERING CHEMISTRY
Module 5- Energy storage devices – Oxygen sensor
Class content:
Oxygen sensor
  Applications
    Oxygen sensor in automobiles
      Principle
      Construction and working

## Slide 3
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Oxygen sensor
Oxygen sensor
An electronic device that measures the proportion of O2 in the gas or liquid being analysed
Applications of O2 sensor:
Divers use to measure partial pressure of O2 in their
breathing gas
Scientists use as probes to measure respiration or
production of O2
O2 analyzers used in medical applications such as anesthesia
monitors, respirators etc
Used to measure exhaust gas concentrations of O2 in IC
engines

## Slide 4
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Oxygen sensor
Role of oxygen sensor in automobiles
Principle :
Stoichiometric air/fuel ratio ideal for combustion of gasoline is 14.7:1
Located in the exhaust stream and indirectly determine air to fuel ratio
O2 sensor allows engine control system to maintain ideal ratio across various engine operating systems
It compares the amount of O2 in the exhaust to the amount of O2 in the atmosphere

## Slide 5
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Oxygen sensor
An output voltage is generated based on the difference in O2 concentration in the exhaust and atmosphere
An output voltage of 0.2V represents a lean mixture and 0.8V represents a rich mixture
Ideal set point is around 0.45 V
The voltage is sent as feedback to Engine control unit which adjusts the air/fuel ratio back to stoichiometric value
Lean mixture results in more of NOX emissions
Rich mixture leads to more of CO , C particles and unburnt
fuel emissions
Based on solid state electrochemical fuel cell
Operates at a minimum temperature of 360oC

## Slide 6
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Oxygen sensor
Construction:
Anode : Pt
Cathode : Pt
Electrolyte : Zirconium oxide (ZrO2 )
doped with Yttrium oxide (Y2O3 )

## Slide 7
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Oxygen sensor
Working :
where P1 and P2 are the partial pressures of O2 in
reference air and exhaust gas respectively
Cell voltage is given by

## Slide 8
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Oxygen sensor
Automobiles fitted with O2 sensor must use unleaded
gasoline as lead poisons the Pt catalyst and reduces its
efficiency
Symptoms of failure are – increased tail pipe emissions,
increased fuel consumption and hesitation on acceleration

## Slide 9
Class Content :
GLUCOSE SENSOR
Components of glucose biosensor
Working of glucose biosensor
Limitations
ENGINEERING CHEMISTRY
Module 6- Electrochemical Sensors

## Slide 10: ENGINEERING CHEMISTRY Module VI- Electrochemical Sensors
Blood Glucose Monitoring
Blood Glucose Monitoring is a way of checking the concentration of glucose in the blood using a glucometer.
Provides quick response to tell if the sugar is high or low indicating a change in diet, exercise or insulin.
Over time, it reveals individual of blood glucose changes.

## Slide 11: Why Monitor Blood Glucose?
ENGINEERING CHEMISTRY
Module VI- Electrochemical Sensors
Reduces risk of developing complications with diabetes.
Allows diabetics to see if the insulin and other medications they are taking are working.
Gives diabetics an idea as to how exercise and food affect their blood sugar.
May prevent hypoglycemia or hyperglycemia

## Slide 12
Analyte
Bioreceptor
Transducer
Electronics and display
ENGINEERING CHEMISTRY
Module 6- Electrochemical Sensors
Components of Glucose Sensor

## Slide 13: ENGINEERING CHEMISTRY Module VI- Electrochemical Sensors
Working of Glucose Biosensor
Developed by Updike and Hicks
Enzyme Glucose oxidase(GOx) catalyze the oxidation of glucose by molecular oxygen producing glucolactone and hydrogen peroxide.
In order to work as a catalyst, GOx requires a redox cofactor –flavin adenine dinucleotide (FAD), works as an initial electron acceptor and is reduced to FADH2.
Glucose + GOx –FAD+  Glucolactone + GOx – FADH2

## Slide 14
The cofactor is regenerated by reacting with oxygen, leading to the formation of hydrogen peroxide
GOx – FADH2 + O2  GOx – FAD + H2O2
Hydrogen peroxide is oxidized at a platinum electrode.
The number of electron transfers, at electrode surface is directly proportional to the number of glucose molecules present in the blood.
H2O2  2H+ +O2 + 2e-
ENGINEERING CHEMISTRY
Module VI- Electrochemical Sensors
Working of Glucose Biosensor

## Slide 15
ENGINEERING CHEMISTRY
Module 6- Electrochemical Sensors
Working of Glucose Biosensor

## Slide 16
ENGINEERING CHEMISTRY
Module VI- Electrochemical Sensors
Limitations of Glucose Sensors
Extreme environmental conditions like haematocrit values, or medication interferences may potentially falsify blood glucose readings.
Incorrect blood glucose readings may lead to treatment errors, for example, incorrect insulin dosing.

## Slide 17
Asha A
Department of Science and Humanities
THANK YOU