## Slide 1
Asha A
Department of Science and Humanities
ENGINEERING CHEMISTRY

## Slide 2
ENGINEERING CHEMISTRY
Module 5- Energy storage devices – Fuel cells
Class content:
H2 – O2 alkaline fuel cell
  Principle
  Construction and working
  Advantages
  Disadvantages

## Slide 3
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Fuel cells
Alkaline fuel cells
Aqueous solution of KOH is used as electrolyte
Low temperature fuel cell (operates at 100oC)
Oxygen reduction is more rapid in alkaline electrolytes
than in acid electrolytes
Use of non noble metal electro-catalyst is feasible
Carbon containing fuels cannot be used as CO2 is
formed as product which reacts with the electrolyte, KOH, to form K2CO3 which reduces efficiency of the cell
CO2 + KOH  K2CO3 + H2O

## Slide 4
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Fuel cells
Construction :
Anode : Porous carbon impregnated with Pt catalyst
Cathode : Porous carbon impregnated with Ag catalyst
Fuel : Hydrogen gas
Oxidant : Oxygen gas
Electrolyte : 30-45 % KOH(warm)

## Slide 5
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Fuel cells
Source:https://www.intechopen.com/books/new-trends-in-ion-exchange-studies/hydroxide-transport-in-anion-exchange-membranes-for-alkaline-fuel-cells
Cell representation:
H2 Pt KOH Ag O2

## Slide 6
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Fuel cells
H2 gas diffuses through anode ,gets adsorbed on the electrode surface ,reacts with OH- to form water
At cathode O2 diffuses through electrode, is adsorbed and reduced to OH-
Product is water which dilutes the KOH
Cell operates at 100oC, so that water from KOH escapes as steam
The water was used by astronauts for drinking on Apollo spacecraft
Emf = 1.23 V
Working:

## Slide 7
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Fuel cells
Advantages:
Operates at low temperature
Alkali is used as electrolyte hence non noble metal catalyst can
be used so less expensive
Disadvantages:
Reactants must be free from C, because on oxidation CO2 is formed .The alkali reacts with CO2 to form carbonates which reduce efficiency of the cells; pure fuel and oxidant which are free of carbon compounds must be used
Liquid electrolytes pose handling problems

## Slide 8
Asha A
Department of Science and Humanities
THANK YOU