## Slide 1
Asha A
Department of Science and Humanities
ENGINEERING CHEMISTRY

## Slide 2
ENGINEERING CHEMISTRY
Module 5- Energy storage devices – Numericals
Class content:
Numericals
  Battery Characteristics
  Efficiency of Fuel cells

## Slide 3
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Numericals
1. A battery using Zn as anodic material lasts for 2 hours when a constant current of 1.25 A is drawn from it. What weight of Zn is present in the battery if the reaction at the anode is
If the electricity storage density of the battery is 180 As/g, determine the weight of the entire battery.
(Given : molar mass of Zn = 65 g, F = 96500 C/mol)
Sol.

## Slide 4
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Numericals
2. Calculate the electricity storage density of lithium battery which stores 2.0 g of lithium. The total weight of the battery is 65 g. Give the answer in Ah/kg.
(Given : Atomic mass of lithium is 7)
Sol.

## Slide 5
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Numericals
3. Calculate the energy density and power density of 20 kg lead acid battery which contains 5 kg anode material and discharges constant current for 10 hours. The voltage of the battery is 2 V. (Given : Atomic mass of lead is 207.2, number of electrons transferred in the redox reaction is 2, F= 96500 C/mol)
Sol.

## Slide 6
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Numericals
4. Calculate the efficiency of H2-O2 alkaline fuel cell
[Given: EoCell =1.20 V, = -285.8 kJ/mole]
Sol.

## Slide 7
ENGINEERING CHEMISTRY
Module 5- Energy Storage devices- Numericals
5. If EoCell for H2-O2 alkaline fuel cell is 1.23 V and efficiency is 83%, calculate the heat evolved during the reaction.
Sol.

## Slide 8
Asha A
Department of Science and Humanities
THANK YOU