## Slide 1
HARISH N
Department of Science and Humanities
ENGINEERING CHEMISTRY

## Slide 2
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
Class content:
Molecular weight of polymers
  Number average molecular weight
  Weight average molecular weight
  Viscosity average molecular weight

## Slide 3
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
Molecular weight of Polymers
Polymers are a mix of chains of different lengths
Weight of polymers is expressed as an average molecular weight
The molecular weight is an important characteristic of a polymer sample as several properties of polymers depend on the molecular weight
The entire range of mechanical properties like stress-strain, impact, fracture, fatigue, creep, stress relaxation and cracking are influenced by average molecular weight and molecular weight distribution

## Slide 4
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
Average molecular weight
Number average molecular weight
Weight average molecular weight
Viscosity average molecular weight

## Slide 5
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
Number average molecular weight,
Obtained by dividing the total weight of the dispersed material with the total number of polymer units present
where n1, n2, n3 …. are number of polymer units having molecular weights M1, M2, M3,…. respectively
where ni is the number of polymer units of molecular mass Mi
It depends only on number of polymer units and not their size
Colligative properties like osmotic pressure, elevation in boiling point or depression in melting point is used to determine number average molecular weight

## Slide 6
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
Weight average molecular weight,
It gives representation to various molecular species in
proportion to their masses in the given material
In the averaging process, the molecular weight of each
individual species is multiplied by its mass
where m1, m2, m3 …. are masses of polymer units having molecular weights M1, M2, M3 respectively

## Slide 7
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
if n1, n2, n3 …. are number of polymer units having
molecular weights M1, M2, M3 respectively
then m1 = n1M1, m2 = n2 M2 ….
Weight average molecular weight can be written as
It depends on size of the polymer units
Properties which depend on size like sedimentation
velocity or light scattering are used to determine weight
average molecular weight

## Slide 8
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
The ratio is called the polydispersity index (PDI)
It is a measure for the broadness of a molecular weight distribution of a polymer, that is, the larger the polydispersity index, the broader the molecular weight distribution
A monodisperse polymer where all the chain lengths are equal has PDI =1
PDI > 1, shows that the polymeric sample is less homogeneous and polydisperse
Source:http://employees.csbsju.edu/cschaller/Advanced/Polymers/CPmw.html

## Slide 9
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
Viscosity average molecular weight,
a is the Mark- Houwink parameter
its value depends on the polymer- solvent system at a particular temperature and is 0.5≤ a ≤ 0.9
Viscosity average molecular weight is closer to weight average molecular weight as larger molecules contribute more to viscosity

## Slide 10
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
Source:https://link.springer.com/chapter/10.1007/978-3-642-38730-2_2
> >
Molecular weight distribution curve

## Slide 11
ENGINEERING CHEMISTRY
Module 7- Functional materials-Polymers
End of Module 7

## Slide 12
HARISH N
Department of Science and Humanities
harishn@pes.edu
THANK YOU