## Slide 1
ELEMENTS OF ELECTRICAL ENGINEERING
UE24EE141B
Renuka Kajur
Department of Electronics and Communication Engineering

## Slide 2
ELEMENTS OF ELECTRICAL ENGINEERING UE24EE141
Concept of Ideal Sources, Kirchhoff’s Laws
Renuka Kajur
Department of Electrical & Electronics Engineering

## Slide 3
Ideal Voltage Source
ELEMENTS OF ELECTRICAL ENGINEERING
Its terminal voltage is independent of current flowing through it.
The current delivered by it depends on the circuit to which it is connected.
When R = 10Ω, IS = 1.2A
When R = 1Ω, IS = 12A

## Slide 4
Ideal Current Source
ELEMENTS OF ELECTRICAL ENGINEERING
Its current is independent of the voltage across it.
The voltage across it depends on the circuit to which it is connected.
When R = 1Ω, VS = 1V
When R = 10Ω, VS = 10V

## Slide 5
Kirchhoff’s Current Law (KCL)
ELEMENTS OF ELECTRICAL ENGINEERING
KCL States “At every node in an electric network, the algebraic sum of currents is Zero (or) sum of incoming currents is equal to the sum of outgoing currents”.
A point at which two or more elements are interconnected is a node.
KCL signifies the conservation of charge.
By KCL at node A,
I1 + I4 = I2 + I3

## Slide 6
Kirchhoff’s Voltage Law (KVL)
ELEMENTS OF ELECTRICAL ENGINEERING
KVL States “Around every closed path in an electric network, the algebraic sum of voltages is Zero”.
A path in an electrical network which starts and ends at the same terminal is called a closed path.

## Slide 7
Kirchhoff’s Voltage Law (KVL)
ELEMENTS OF ELECTRICAL ENGINEERING
Conventionally, Voltage drop is considered negative and voltage rise as positive.
KVL signifies conservation of energy.
KVL in the path ABDA:
-V1-V3+Va = 0
KVL in the path BCDB:
V2-Vb+V3 = 0
KVL in the path ABCDA:
-V1+V2-Vb +Va = 0

## Slide 8
Numerical Example on KVL
ELEMENTS OF ELECTRICAL ENGINEERING
Example 1:
Find the current through 8Ω resistor in the network given.

## Slide 9
Numerical Example on KVL
ELEMENTS OF ELECTRICAL ENGINEERING
Solution:
KVL: +10-8I-6-8+12 = 0
Hence, I = 1A

## Slide 10
Numerical Example on KVL
ELEMENTS OF ELECTRICAL ENGINEERING
Example 2:
Find the voltage VAB in the network shown:

## Slide 11
Numerical Example on KVL
ELEMENTS OF ELECTRICAL ENGINEERING
Solution:
KVL (AXYCA): +20-5I1-3I1-2I1 = 0; Hence, I1 = 2A
KVL (BZEB): +40-5I2-5I2 = 0; Hence, I2 = 4A
KVL (ACDEBA): +2I1-10-5I2+VAB = 0; Hence, VAB = 26V

## Slide 12
Numerical Example on KVL
ELEMENTS OF ELECTRICAL ENGINEERING

## Slide 13
Text Book & References
ELEMENTS OF ELECTRICAL ENGINEERING
Text Book:
“Electrical and Electronic Technology” E. Hughes (Revised by J. Hiley, K. Brown & I.M Smith), 11th Edition, Pearson Education, 2012.
Reference Books:
1. “Basic Electrical Engineering”, K Uma Rao, Pearson Education, 2011.
2. “Basic Electrical Engineering - Revised Edition”, D. C. Kulshreshta, Tata- McGraw-Hill, 2012.
3. “Engineering Circuit Analysis”, William Hayt Jr.,
Jack E. Kemmerly & Steven M. Durbin, 8th Edition,
McGraw-Hill, 2012.

## Slide 14
renukark@pes.edu
THANK YOU
Renuka r kajur
Department of Electronics and Communication Engineering