## Slide 1
ELEMENTS OF ELECTRICAL ENGINEERING
UE24EE141B
RENUKA R KAJUR
Department of Electrical & Electronics Engineering

## Slide 2
ELEMENTS OF ELECTRICAL ENGINEERING UE24EE141
Practical Sources & Source Transformation
Renuka r Kajur
Department of Electronics and communication Engineering

## Slide 3
Practical Voltage Source
ELEMENTS OF ELECTRICAL ENGINEERING
Its terminal voltage falls as load current increases.
It is modelled as an ideal voltage source in series with
internal resistance.
Internal resistance is small, usually few mΩ.
Internal resistance of an ideal voltage source is Zero

## Slide 4
Practical Voltage Source
ELEMENTS OF ELECTRICAL ENGINEERING
V = VS – I*RS

## Slide 5
Practical Current Source
ELEMENTS OF ELECTRICAL ENGINEERING
Its terminal current falls as load voltage increases.
It is modelled as an ideal current source in parallel with
internal resistance.
Internal resistance is very high, usually few Mega Ohms
Internal resistance of an ideal current source is Infinite

## Slide 6
Practical Current Source
ELEMENTS OF ELECTRICAL ENGINEERING
I = IS – ()

## Slide 7
Numerical Example on Practical Sources
ELEMENTS OF ELECTRICAL ENGINEERING
Question:
A battery of EMF 12V and internal resistance of 0.05Ω supplies power to a load resistance RL. Determine the % change in load voltage as load resistance varies from 10Ω to 100Ω.
Solution:
Case 1: RL = 10Ω
V = = 11.94V
(By Voltage Division)

## Slide 8
Numerical Example on Practical Sources
ELEMENTS OF ELECTRICAL ENGINEERING
Solution (Continued..):
Case 2: RL = 100Ω
V = = 11.99V
% Change in the load voltage = *100 = 0.42%

## Slide 9: Numerical Example on Practical Sources

## Slide 10
Source Transformation
ELEMENTS OF ELECTRICAL ENGINEERING
A Practical Voltage Source can be transformed to a Practical Current Source & Vice versa.
Two Sources are equivalent if they supply same terminal voltage and current when loaded with same load resistance.

## Slide 11
Source Transformation
ELEMENTS OF ELECTRICAL ENGINEERING
Case 1: Open Circuit Condition
V = VS
V = IS*RS
Hence, VS = IS*RS

## Slide 12
Source Transformation
ELEMENTS OF ELECTRICAL ENGINEERING
Case 2: Short Circuit Condition
I =
I = IS
Hence, VS = IS*RS

## Slide 13
Numerical Example on Source Transformation
ELEMENTS OF ELECTRICAL ENGINEERING
Question:
Find the current through 5Ω resistor in the network shown:
Solution:
Replace 3A current source & 2Ω resistance with equivalent practical voltage source.
Repeat the same for 2A current source & 1Ω resistance.

## Slide 14
Numerical Example on Practical Sources
ELEMENTS OF ELECTRICAL ENGINEERING
Solution (Continued..):
+6-2I – 5I – I+2 =0
I = 1A
By applying KVL

## Slide 15
Source Transformation
ELEMENTS OF ELECTRICAL ENGINEERING

## Slide 16
Text Book & References
ELEMENTS OF ELECTRICAL ENGINEERING
Text Book:
“Electrical and Electronic Technology” E. Hughes (Revised by J. Hiley, K. Brown & I.M Smith), 11th Edition, Pearson Education, 2012.
Reference Books:
1. “Basic Electrical Engineering”, K Uma Rao, Pearson Education, 2011.
2. “Basic Electrical Engineering - Revised Edition”, D. C. Kulshreshta, Tata- McGraw-Hill, 2012.
3. “Engineering Circuit Analysis”, William Hayt Jr.,
Jack E. Kemmerly & Steven M. Durbin, 8th Edition,
McGraw-Hill, 2012.

## Slide 17
renukark@pes.edu
THANK YOU
Renuka
Department of Electrical & Electronics Engineering